## Slide 1: Project of Computer Networks： Implementation of a DNS Relay

## Slide 2: Outline
Basic requirements
What is DNS
How to use Wireshark
How to make socket programming

## Slide 3: DNS Relay
Receiving DNS queries from DNS client (Resolver) and forward them to a given DNS server
Receiving DNS responses from DNS server and forward them to the Resolver
Resolver
DNS Relay
DNS Server
Query
Query
Response
Response

## Slide 4: 3 Cases
Checking local database (eg. dnsrelay.txt) first
  Case 1: for IP address 0.0.0.0, sending back “no such name” (reply code =0011)
  Case 2: for domain name included in the database, sending back corresponding IP address
  Case 3: for domain name not included in the database, forward query to local DNS server

## Slide 5: Environment
OS:
  Windows or Linux
Programming language:
  C, C++, Java,Python,…
Working in a group
  3 persons
  1 source program and 1 report

## Slide 6: Getting started Understanding DNS
Domain Name System
A distributed database providing mapping between Domain name and IP address
  Implemented in hierarchy of many name servers
An application protocol
  Used by hosts and name servers to communicate to resolve names
Mostly using UDP in transport layer

## Slide 7: Domain Namespace – the hierarchical structure
com
edu
gov
int
mil
net
org
ae
cn
zw
mit
cs
xx
cs
edu
bupt
…
…
Generic domains
Top level domains
2nd level domains
xx.cs.mit.edu
cs.bupt.edu.cn
Unnamed root
Country domains

## Slide 8: Name Servers
Name servers are the repositories of information that make up the domain database.
Answering queries about name information

## Slide 9: DNS Clients: Resolvers
The interface between the user program and the domain name servers
  A resolver receives a request from a user program (e.g., HTTP, mail programs, TELNET, FTP，Ping)
  Asks questions to the DNS system on behalf of the application
  And returns the desired information
Notes: gethostbyname

## Slide 10: eg. DNS working together with the HTTP application
User types in or click on a URL
Browser extracts the site name
Browser calls resolver to learn IP address
Query the local DNS server
Gets a reply
Browser
Resolver
Web server
Contacts the Web server

## Slide 11: Name information: Resource Records
Each domain in the DNS has one or more Resource Records (RRs), which are fields that contain information about that domain
Each RR has the following information
  Owner: the domain name where the RR is found
  Type: specifies the type of the resource in this RR
    A – Host Address
    MX – Mail Exchanger
    …
  Class: specifies the protocol family to use
    IN – the Internet system
  TTL: specifies the Time To Live (in unit of second) of the cached RRs
  RDATA: the resource data

## Slide 12: Caching mechanisms
Caching at the name servers
Caching at the hosts

## Slide 13: Protocol details: Message Format (from RFC 1035)
13
Header
Question Section
Answer Section
Authority Section
Additional Section
ID | QR | OPCODE |  |  |  |  | Z | Rcode
Question count | Answer count |  |  |  |  |  |  | 
Authority count | Additional count |  |  |  |  |  |  | 
31
16
15
0
(variable number of questions)
(variable number of Resource Recordss)
AA TC RD RA
Fixed length
Variable length
(variable number of Resource Recordss)
(variable number of Resource Recordss)
Flags

## Slide 14: DNS Message Header Structure(1)
ID: 16-bit field used to correlate queries and responses.
QR: 1-bit field that identifies the message as a query (0) or response (1).
OPCODE: 4-bit field that describes the type of query:
  0: Standard query (name to address). 1: Inverse query (address to name). 2: Server status request.
AA: Authoritative Answer. 1-bit field. When set to 1, identifies this response is made by an authoritative name server.
TC: Truncation. 1-bit field. When set to 1, indicates the message has been truncated due to length greater than that permitted.
RD: Recursion Desired. 1-bit field. Set to 1 by the resolver to request recursive service by the name server.
RA: Recursion Available. 1-bit field. Set to 1 by name server to indicate recursive query support is available.
Z: 3-bit field. Reserved for future use. Must be set to 0.

## Slide 15: DNS Message Header Structure(2)
RCODE: Response Code. 4-bit field that is set by the name server to identify the status of the query:
  0: No error condition. 1: Unable to interpret query due to format error. 2: Unable to process due to server failure. 3: Name in query does not exist. 4: Type of query not supported. 5:Query refused for policy reasons.
QDCOUNT(Question count): 16-bit field that defines the number of entries in the question section.
ANCOUNT(Answer count): 16-bit field that defines the number of resource records in the answer section.
NSCOUNT(Authority count): 16-bit field that defines the number of name server resource records in the authority section.
ARCOUNT(Additional count): 16-bit field that defines the number of resource records in the additional records section.

## Slide 16: Question Section Format
QEURY DOMAIN NAME (variable number of domain names) | 
QUERY TYPE | QUERY CLASS
QUERY TYPE: 16-bit field used to specify the type of the query
  A(1) – Host address
  MX(15) – Mail exchanger for the domain
  …
QUERY CLASS: 16-bit field used to specify the class of the query
  IN(1) – Internet system
  …
31
16
15
0

## Slide 17: Resource Record Format (1)
DOMAIN NAME | 
TYPE | CLASS
TTL | 
RESOURCE DATA | 
RESOURCE DATA LENGTH
31
16
15
0

## Slide 18: Resource Record Format (2) – type field
SOA
  Start Of Authority--identifies the domain or zone and sets a number of parameters
NS
  Maps a domain name to the name of a computer that is authoritative for the domain
A
  Maps the name of a system to its address. If a system (e.g., a router) has several addresses, then there will be a separate record for each.
AAAA
  Maps the name of a system to its IPv6 address. If a system (e.g., a router) has several addresses, then there will be a separate record for each.
CNAME
  Maps an alias name to the true, canonical name
MX
  Mail Exchanger. Identifies the systems that relay mail into the organization

## Slide 19: Resource Record Format (3) – type field
TXT
  Provides a way to add text comments to the database. For example, a txt record could map abc.com to the company's name, address, and telephone number
WKS
  Well Known Services. Can list the application services available at the host. Used sparingly, if at all
HINFO
  Host Information, such as computer type and model. Rarely used
PTR
  Maps an IP address to a system name. Used in address-to-name files.

## Slide 20: Example of Resource Records(1)
Type=NS
  Name= Domain, eg. bupt.edu.cn
  value= Domain name of Authoritative Name Server
Type=A
  Name= Domain name , Value= IP Address
ns.bupt.edu.cn 86400 IN A 202.112.10.37
bupt.edu.cn 86400 IN NS ns.bupt.edu.cn

## Slide 21: Example of Resource Records (2)
Type=CNAME
  Name= canonical name
  Value= the name
  Type=MX
    Name= Domain name
    Value= canonical name of mail server
dns.bupt.edu.cn 86400 IN CNAME ns.bupt.edu.cn
bupt.edu.cn 86400 IN MX mail.bupt.edu.cn

## Slide 22: DNS tools: nslookup
Query type=A
Query type=MX

## Slide 23: Using wireshark to understand the communications
Wireshark: A network protocol analyzer (packet sniffer)
Able to capture packets transferred on the network and display packet fields and their meanings
Used for network troubleshooting, analysis, software and communications protocol development, and education.

## Slide 24: Download Wireshark
Official website
  http://www.wireshark.org/
Download page
  http://www.wireshark.org/download.html

## Slide 25: Starting wireshark in windows
Select Interface, set Capture Filter, then press Start
以管理员身份运行
Notes: Vista和Win7环境下，需要以管理员身份运行wireshark,
或者在command环境(管理员身份运行)下，运行 net start NPF

## Slide 26: How to initiate the communications?
DNS
  Start Wireshark
  You can access a website in your browser
  Or you can use nslookup in command line

## Slide 27
display filter
A DNS query message
Notes: dns

## Slide 28
A DNS response message

## Slide 29: Using Socket programming
Socket: an extension to OS’s I/O system, enabling communication between processes and machines
A interface (a “door”) into which application process can both send and receive messages to/from another (remote or local) application process

## Slide 30: Socket programming using UDP
Socket: a door between application process and end-end transport protocol (UDP or TCP)
UDP service: unreliable transfer of datagram from one process to another
controlled by
application
developer
controlled by
operating
system
Client
controlled by
application
developer
controlled by
operating
system
Server
Internet
process
UDP with
buffers,
variables
socket
process
UDP with
buffers,
variables
socket

## Slide 31: Overview of UDP-based sockets API
socket()
socket()
bind()
recvfrom()
sendto()
sendto()
recvfrom()
close()
UDP Client
UDP Server
data
data

## Slide 32: Running the program (1)
    1. Get the IP address of your DNS server (eg. 202.106.0.20 ) and your IP address (eg. 192.168.0.104 )
c:> ipconfig /all
    2. configure your DNS server as your IP address (eg. 192.168.0.104 or 127.0.0.1)
Notes: ipconfig

## Slide 33: Running the program (2)
3. Running your program, setting local DNS server as 202.106.0.20
4. using ,nslookup, ping，web browser… to test your program

## Slide 34: Example implementation
Command
dnsrelay [-d | -dd] [dns-server-ipaddr] [filename]

## Slide 35: About project reports
Following contents shall be included:
  Requirement analysis
  Decomposition of functional modules
  Overall flow chart
  Flow charts in each module
  Testing and results
  Summary of works and future improvement

## Slide 36: Deadline
Evaluation
  8:30-16:20, July 16(calss17/18)
  17(calss19/20)
  18 (class21/22)
Report
  Packing and email to gaozc@bupt.edu.cn before 0 o’clock July 12
  Named as studentID1Name-ID2Name-ID3Name.pdf or doc